## Slide 1: Cave map generation from 3D models “A small matter of math and programming, with a sprinkling of AI”
Jari Arkko
November 27, 2021

## Slide 2: Background
Introduction of consumer devices that – in principle – make 3D modelling possible
Could I use this technology to more easily explore and document caves?
  Example: my Finnish cave map count: 100+ (maybe 5%)
In practice there’s a lot of obstacles: technique, lightning, applications, software, scaling, limits of accuracy
A lot of interesting problems for researchers 

## Slide 3: The Model Problem
I thought that we’d be done once there’s a model
Gives an overview of the cave
Can be used for navigation in the cave
Has all the details needed

## Slide 4: The dream is that models are everything

## Slide 5: Nice straight tunnels
Lummelunda, Sweden

## Slide 6: But: In practice it is often messy

## Slide 7: Or even messier – I don’t know how to put these pieces together…
Kraljičina spilja (Queen’s Cave), Croatia
(Where are the stalactites here, by the way?)

## Slide 8: Going beyond 3D
Models are not easy to deal with in all situations
  For many situations I’d prefer a simpler plan view
  I thought I can just do intersection in my 3D tools… not so
Can we generate a map algorithmically?
New software to take slices or plan views of 3D models
  https://github.com/jariarkko/cave-outliner

## Slide 9: Sketch for an approach
Take a model as input
Reduce information content (outlines vs. structure etc)
Provide suitable views (plan, x-section)
Apply feature recognition algorithms
  Topological
  Heuristics
  ML
Grottberget, Siuntio

## Slide 10: Some complications
Going through 10^7+ objects is expensive => search structures
Math sounds relatively easy, but … is (x,y) in triangle?
Models are imperfect – algorithms for filling holes
What’s a definition of an entrance?
Nothing above - outside
1 layer - odd
2 layers - tunnel
Dripline – empty/rock interface above the entrance
Height, width, depth sufficient into the tunnel part
Empty in front
Not part of cave!
Here entrance is from the left
But could be to any direction
Including down… also up?
Holes in roof are different!

## Slide 11: Example plan view

## Slide 12: Example plan view

## Slide 13: Example cross section view

## Slide 14: Longitudinal cross-section

## Slide 15: Machine-learning
Could perhaps be recognised as rocks?
Work in progress
Feeding 2D images (e.g., depthmaps as here)
Or feeding 3D models (expensive and hard)
Likely only bigger features can be recognised